## Slide 1
Building a Solar Generator KC4WGA – Carl Fenske
KC4WGA@gmail.com

## Slide 2: Why Build a Solar Generator?
Portable Operation
Emergency Power
Field Day – ARRL
Winter Field Day
Jamboree-on-the-Air (BSA)

## Slide 3: Why Build a Solar Generator?
Notes: Winter Field Day 2018

## Slide 4
Easily available
More power for lower cost
Need to store fuel
Carbon monoxide
Difficult to start
Gasoline Generators
Solar Generators
Comparing Gasoline and Solar Generators
Low upkeep
Higher initial cost
No fuel to store
Clean and quiet
Weather dependent

## Slide 5: Components of a Solar Generator
Solar Panels
Charge Controller
Battery and Charger
DC/AC Power Inverter

## Slide 6: Solar Panels
PV panel should be sized to match the capacity of battery and charge controller
100W Solar Panel
  Open-Circuit Voltage: 24.3V
  Short-Circuit Current: 5.21A
Notes: My Charge Controller:
Maximum 100V
Maximum 20A

## Slide 7: Solar Charge Controllers
Regulates the power going from the solar panels to the batteries
PWM: Simpler circuitry; less efficient; less expensive; light weight
MPPT: High voltage panels can be used to charge a 12/24/48v battery bank; converts excess voltage into additional amperage; 99+ percent efficient; heavier; more expensive
Notes: PWM: Pulse Width Modulation (examples)
MPPT: Maximum Power Point Tracking

## Slide 8: 30A PWM Charge Controller
Notes: $32
Bluetooth adapter available

## Slide 9: 40A MPPT Solar Charge Controller
Notes: 99+% efficient
Bluetooth adapter available
$112
ML2420N • 20A • 12V/24V • Auto 9V to 35V Battery Voltage • Maximum solar input voltage 100v • 260W/12V 520W/24V • ≤98% efficiency • -35℃ to +45℃ IP32 RS232 ≤ 3000m 210*151*59.5mm ML2440N10 40A 550W/12V 1100W/24V 238*173*72.5mm 238*173*72.5mm 1.4Kg

## Slide 10: Renogy BT-1 Bluetooth Module
Notes: Renogy BT-1 Bluetooth module
$32

## Slide 11: Deep-Cycle Batteries
Sealed Lead-Acid (SLA)
  Gel Cell
  AGM (Absorbent Glass Matt) batteries
Li-Ion (lithium-Ion)
LiFePO4 (lithium-iron-phosphate)
LiFeMgPO4 (lithium-iron-magnesium-phosphate)

## Slide 12: Benefits of AGM Batteries
Good option for Ham radio use
Sealed - low maintenance; won’t spill
Heavy
Less expensive

## Slide 13: Benefits of LiFePO4 Batteries
Nearly twice the run-time and a half the mass of a comparatively sized lead-acid battery
Handles high loads better, less voltage drop
May last as long as 3,000 cycles
Nearly maintenance-free
Mounts any orientation, but up recommended
Less fire danger than earlier lithium designs

## Slide 14: Comparing Useful Energy Density
Sealed Lead-Acid Battery (12.8V 14Ah)
  179W x .5 = 84 / 5.0Kg = 18W/Kg
Valence LiFeMgPO4 Battery (13.2V 40Ah)
  528W x 0.8 = 422 / 6.1Kg = 69W/Kg
Calb LiFePO4 Cell (3.2V 72Ah)
  230W x .8 = 184 / 1.8Kg = 102W/Kg
Notes: 3.8 times more efficient/Kg

## Slide 15: Inventus 12.8v 45Ah LiFePO4 Batteries

## Slide 16: Inventus 12.8v 45Ah LiFePO4 Batteries
Medical Grade Batteries with BMS
Professionally Tested:
  80-89% - $125
  90-99% - $150
Notes: 12.8V x 45Ah x 573W
Charge and and discharge up to 20 amps continuous.

## Slide 17: Charging a LiFePO4 12V Battery
Bulk/Absorb: 14.2 – 14.6 Volt; 0 – 2 hours
High charge rate: Capacity/2 (40AH/2 = 20A)
Float: 13.6 Volt or less
Best to stored at a partial charge

## Slide 18: 48V 10A Variable Power Supply
Notes: Use this adjustable power supply with your charge controller is the best universal battery charger.
$40

## Slide 19: Charging a LiFePO4 12V Battery

## Slide 20: Discharging a 45AH LiFePO4 Battery
Maximum continuous discharge: 20 A
Maximum 10 second current pulse: 28 A
Cut-off Voltage: 10V
Run-time @ 10A: 240 minutes
Run-time @ 20A: 120 minutes
Run-time @ 23A: 100 minutes
100W HF radio: 180 minutes

## Slide 21: Discharging an LiFePO4 Battery

## Slide 22: Battery Management System (BMS)
Protects from over charge/discharge
Limits charge/discharge currents
Monitors cell temperatures
Balance the cells during charging
You must still use a charge controller

## Slide 23: For Long LiFePO4 Battery Life
Keep the battery temperature under 30˚C
Charge battery above 0˚C
Keep charge/discharge currents under 50% capacity; 20% preferred
Do not cycle battery below 10-15% SOC
Do not float the battery at 100% SOC

## Slide 24: Power Inverters - Converts DC to AC current
Pure Sine Wave Inverter
  Clean power; household AC
  Better for motors and electronics
  Greater efficiency
Notes: A true sine wave contains the harmonic distortions of the carrier frequency. In other words, it is not a "smooth" sinewave. I believe that in order for an inverter to claim "True Sinewave" output, these ripple distortions must be below 3%.

## Slide 25: Power Inverters - Converts DC to AC current
Modified Sine Wave Inverter
  Simulates sine wave
  Not compatible with many devices
  Less expensive

## Slide 26
Battery chargers
Variable speed tools
Electric shavers
Newer TV’s
Some laptops
Induction cooktops
Items with brushless motors
Coffee makers
Electric blankets
Microwaves
Audio equipment
Laser printers
Many digital clocks
Medical equipment
Common electronic devices that should not be used with a modified sine wave inverter
Notes: I will choose to use a Pure Sine Wave Inverter because of it's universal use and more energy efficient.

## Slide 27: Wiring a Solar Generator

## Slide 28: Solar Generator Block Diagram

## Slide 29: Costs to Build Your Solar Generator
COMPONENT | COST
100 Watt 12V Solar Panel | $110.00
45Ah LiFePO4 Battery (Battery Hookup) | $150.00
Solar Charge Controller 30A PWM | $35.00
500W BESTEK Pure Sine Wave Inverter | $55.00
TOTAL | $350.00

## Slide 30: Resources
https://sunelec.com/home/
http://ki0bk.no-ip.com
https://www.solacity.com/how-to-keep-lifepo4-lithium-ion-batteries-happy/
https:// https://batteryhookup.com/
Craigslist, eBay, Amazon, Newegg, etc.

## Slide 31: Building a Larger-Scale Solar Generator
Back-Up Emergency Power
Off-Grid Power
RV or Camper
Powering medical devices during outages
Power during extended power outages
A level of energy independence

## Slide 32: 12V Battery Systems
ADVANTAGES:
Multiuse: Ham Radio and other 12V applications
Smaller, more portable applications
Familiar and relatively safe, little chance of electrical shock; greater comfort level

## Slide 33: Solar Panels
4 – 290W (used) ET Solar Group Solar Panels
Cells 72 Maximum Power Current: 8.08A
Maximum Power Voltage: 35.92V
77” H 39.1”W x 1.6”D (stationary use)

## Slide 34: 12V Battery Systems
DISADVANTAGES
You can only use smaller 12-volt devices.
Lower voltage and higher amperage requires larger gauge wire which is more expensive.
A 12-volt solar panel loses a lot of its energy when sending it over long distances.

## Slide 35: 24V/48V Battery Systems
ADVANTAGES:
It can accommodate a larger solar array.
You can power more larger AC appliances.
Expandable
It is more cost effective, more efficient, experience less transmission loss, and weighs less.

## Slide 36: 24V/48V Battery Systems
DISADVANTAGES:
You must wear gloves and be extremely careful.
24V/48V can be lethal!

## Slide 37: 24V Battery System
PRISMATIC CELLS:
8 – 3.2V 72 AH cells in series (25.6V)
1.843 kW of power

## Slide 38: Battery Management System (BMS)
Monitoring the battery
Providing battery protection
Estimating the battery’s operational state
Continually optimizing battery performance
Reporting operational status to external devices

## Slide 39: Integrated Components System
COMPONENTS:
50A PWM Solar Charge Controller
1500W Pure Sine Wave Inverter
(Battery Charger)
Notes: Solar Input Voltage Range :30Vdc~60Vdc
Maximum PV Array Wattage: 1200W
Maximum Solar Charge Current: 50A
Rated Power: 1500W
Cells 72 Maximum Power Current: 8.08A
Maximum Power Voltage: 35.92V
4 panels in parallel 35.92V and 32.32A = 1160 W

## Slide 40: Wiring a Solar Generator

## Slide 41: Cost to Build Larger-Scale Generator
COMPONENT | COST
4-290 Watt Solar Panels (used) | $500.00
8-72Ah Prismatic LiFePO4 Cells | $320.00
100A BMS with Temperature Sensor & Bluetooth | $70.00
50A PWM Charge Controller/1500W Sine Inverter | $205.00
TOTAL | $1095.00

## Slide 42: Show & Tell/Questions & Answers